## Slide 1: LEAP-RE RE4AFAGRI
Speaker
Place - institution
xth Month 2023
M-LED
(A «Multi-sectoral Latent Electricity Demand» assessment platform)
An introduction

## Slide 2
Background:
the RE4AFAGRI modelling platform

## Slide 3: THE RE4AFAGRI modelling platform

## Slide 4: M-LED in the RE4AFAGRI modelling platform
M-LED is the energy demand module of the RE4AFAGRI modelling platform

## Slide 5: Electricity demand
A function of:
Different sectors (residential, industrial, agriculture, social/public services)
Different drivers (population, economic development and growth, infrastructure availability)
Space -> geography, land, urban/rural, climate...
Time -> seasonality

## Slide 6: Electricity demand
Tighly connected with:
Water (pumping and supply)
Land-use decisions (agriculture, urbanisation, etc.)
Climate change (adaptation)
...

## Slide 7
M-LED
Introduction

## Slide 8: M-LED: background
Electricity access gap -> still more than 10% of global population (ESMAP 2021)
Energy demand data is crucial for understanding gap and planning solutions, including in power system planning tools
But how to assess a demand that is currently not existent because there is no electricity access infrastructure…
… which would however be there if electricity access was available?
LATENT DEMAND -> dependent on local socio-economic, environmental, infrastructure characteristics
Three main approaches to estimate it:
  Community elicitation through surveys
  Empirical evaluation and similarity analysis (e.g. communities that recently got electricity)
  Needs-based framework (e.g. Amartya Sen’s capabilities)

## Slide 9: Background and Purpose
M-LED: a Multi-sectoral Latent Electricity Demand geospatial data processing platform to estimate electricity demand in communities that live in energy poverty
Main objective: produce spatio-temporally granular estimates of the latent electricity demand in different sectors for entire countries
Contributed to the development: Giacomo Falchetta, Nicolò Stevanato, Davide Mazzoni, Manfred Hafner, Magda Moner-Girona, Paolo Cornali, Su-Min Choi, Francesco Semeria, Emanuela Colombo…
Spring 2019
Spring 2021
September 2022
2023
Begin of R&D
First public “alpha”
Academic paper
Stable, adaptable release
Capacity building workshops

## Slide 10: Technical Overview
M-LED methods:
  Geospatial data processing algorithms
  Appliance-based and needs-driven modelling
  Stochastic variations in electricity demand
  Scenario logic -> economic, demographic and climate pathways impact on future latent demand
M-LED assumptions:
  Discussed with a broad array of stakeholder from different countries of SSA
  Field visits to assess current pattern of appliance ownership and use
  Literature and needs-driven objectives

## Slide 11: Data Inputs & Outputs
Cluster-based output: clusters encapsulate population settelements and surrounding agricultural land
Electricity demand sectors:
Residential
Irrigation
Crop procesing
SMEs
Healthcare facilities
Schools
Hourly, monthly and yearly demand for each sector -> load curves and seasonality

## Slide 12: Example outputs

## Slide 13: Target Users
Target users:
- Policymakers designing electrification plans
- Private infrastructure developers (solar home systems, solar pumps, mini-grids)
- Researchers and scientists in Africa and elsewhere (capacity building workshops to be held in 2023)
Requirements:
- Current alpha version -> requires coding and modelling proficiency…
- September scheduled release -> much more stable and replicable; less proficiency required to run analysis for custom countries / with custom assumptions
- Moreover -> Development of an accessible output data visualization dashboards for policymakers and private developers in progress!

## Slide 14: Use Cases
MLED is currently being used in the RE4AFAGRI project in linkage with other energy access – NEXUS tools/models and in cooperation with local stakeholders in Zambia and in Rwanda
Aim -> understand and quantify linkages and requirements along the climate-water-energy-agriculture-development Nexus to support private investment.

## Slide 15: Geographic Coverage
M-LED pilot implementation -> Kenya, due to data availability and local contacts to conduct surveys.
Implementation currently in progress -> Zambia and Rwanda in the context of EC-H2020 LEAP-RE project, with direct input from local stakeholder.
Vision -> implementation in larger basket of countries and autonomously by African researchers engaged through capacity building workshops held in 2023.

## Slide 16: Complementarity
M-LED output -> perfect match for supply-side electrification assessment tools, e.g. OnSSET, PVGIS, REM…
Moreover, M-LED receives inputs from WaterCROP, a crop evapotranspiration model that suggests the volumes of water to be pumped and supplied to the fields each month to avoid water stress.
Long-standing discussion with OnSSET and EC-JRC PVGIS developers.
Soft-linkages with OnSSET and PVGIS are being carried out for different projects -> e.g. RE4AFAGRI to understand relevance of agricultural demand for electricity supply planning.

## Slide 17: Public Access
Github -> source code https://github.com/giacfalk/RE4AFAGRI_platform
Zenodo -> base package with replication data for Kenya country study https://zenodo.org/record/4741971
Both will be updated in September – December 2022 to a more stable version.

## Slide 18: User Training & Support
Documentation -> alpha version under: https://github.com/giacfalk/M-LED/wiki
Documentation to be updated in Q1 2023 with creation of a ReadTheDocs website.
Capacity building workshops -> to happen in the RE4AFAGRI project context during 2023 in different SSA countries / virtually.
Direct support in case of issues -> falchetta@iiasa.ac.at

## Slide 19: Future Updates
- Major code and data package update forthcoming in late 2022 -> stability, replicability, ease of access to parameters and assumptions
- Features currently being integrated:
  Standalone solar pumps
  Local cost-benefit analysis of irrigation expansion
  Food security implications of irrigation expansion
  Crop processing machinery
- Vision: improve data quality checks with stakeholders and integrate new data products:
  M-LED would strongly benefit from high-resolution maps of cropland patches and crop type
  Geodatabase of schools would improve precision of social infrastructure modelling

## Slide 20
M-LED
Modules

## Slide 21: Structure of M-LED
Preparation modules
MLED.R -> «homepage» of the model
backend.R -> pre-requirements (software packages, configuration, database donwload) of the model
scenario_xxx.R -> data and parameters specific to the selected run (country, scenario)
electricity_access.R ->
create_clusters_voronoi.R ->

## Slide 22: Demand modules: overview
Non-farm SMEs
Residential
Schools and education
Irrigation (pumping)
Mining
Crop processing
Six sectors are currently represented in M-LED
Residential -> household demand of both household who already benefit from electricity access and of households gaining access to electricity in the future
Non-farm SMEs -> commercial activities and small-scale handcraft
Mining -> heavy industry sector
Crop processing -> agricultural load, post-harvest (e.g. Milling) and cold storage of vegetables
Irrigation -> ground and surface water pumping for crop watering
Schools and education -> social infrastructure demand

## Slide 23: Preparation modules: MLED.R

## Slide 24: Preparation modules: backend.R

## Slide 25: Preparation modules: scenario_xxx.R

## Slide 26: Preparation modules: electricity_access.R

## Slide 27: Preparation modules: create_clusters_voronoi.R

## Slide 28: Demand modules: residential.R

## Slide 29: Demand modules: crop_module.R and pumping_module.R

## Slide 30: Demand modules: mining_module.R

## Slide 31: Demand modules: health_education_module.R

## Slide 32: Demand modules: crop_processing_catchment_areas.R

## Slide 33: Demand modules: other_productive.R

## Slide 34: Demand modules: crop_processing.R

## Slide 35: Conclusive modules: cleaner.R

## Slide 36
M-LED
Software, hardware, and data requirements

## Slide 38
M-LED
Running
M-LED

## Slide 40
M-LED
Outputs and results visualisation and interpretation

## Slide 42
M-LED
Scenarios and assumptions customisation

## Slide 44
M-LED
Soft-linkages

## Slide 45: THE RE4AFAGRI modelling platform
Receiving inputs
Providing outputs

## Slide 46: Input linkages of M-LED
WaterCrop
...

## Slide 47: Output linkages of M-LED
OnSSET
...
NEST
...

## Slide 48
M-LED
FAQs

## Slide 49: FAQs
Q1: What is the running time of M-LED?
A1:
Q2: How much does the M-LED database weight?
A2:

## Slide 50
M-LED
Typical issues

## Slide 51
Issue 1:
Solution 1:
Issue 2:
Solution 2:

## Slide 52
M-LED
How do I run M-LED for my country / region of interest?

## Slide 53: Implementation of M-LED in a new region
Look for data. Country specific datasets which are non included in the SSA-wide database of M-LED include:
A
B
C
D
E

## Slide 54: Implementation of M-LED in a new region
Discuss with stakeholders. Assumptions (socio-economic, technological, scenario and policy) must be tailored.
A
B
C
D
E

## Slide 55: Implementation of M-LED in a new region
Customise parameters in the scenario file. Assumptions (socio-economic, technological, scenario and policy) must be tailored.
A
B
C
D
E

## Slide 56: Implementation of M-LED in a new region
Revise RAMP appliance baskets and usage patterns. What type of appliances will newly electrified household and facilities use, and with what patterns?
A
B
C
D
E

## Slide 57
M-LED
Contact and help

## Slide 58: Contact
For other queries and engagement, reach out to:
re4afagri@gmail.com
https://github.com/giacfalk/RE4AFAGRI_platform

## Slide 59: Contact
For other queries and engagement, reach out to:
re4afagri@gmail.com
https://github.com/giacfalk/RE4AFAGRI_platform